## Slide 1: Google Calendar Assistant
Mihai Cania
Ac CTI-eng an 3

## Slide 2: Purpose and Description
The purpose of this project is to have a small device that can add calendar entries using voice commands and to notify the user if there are upcoming events in the next minutes.
Why that? Because it easier and faster to add an entry using only voice commands, there will be no necessity for a monitor, keyboard, mouse, only the Raspberry PI with a microphone and a speaker
Maybe your calendar is shared with other people, like coworkers, and they add new events. It is a big possibility for the user to miss that, but using this device it will be easy to get a notification about an upcoming event and you won’t miss it.

## Slide 3: System Overview
The Raspberry PI communicate via WIFI with the Router in order to have access to the internet
Calendar polling script have the responsibility to pull events from Google Calendar every minute and if the event starts in the following 10 minutes then the user will be notify by a sound

## Slide 4: System Overview
Google Assistant is integrated in the system and the user can add new calendar entries simply by speaking to it
Google Assistant and Google Calendars communicate one with each other and the calendar entry will be visible in the calendar

## Slide 5: Circuit Design
The hardware view of the system is represented by a Raspberry PI 3 Model B+
It is mandatory to have a microphone connected via USB to the Raspberry PI
A sound device must be connected also via USB, AUX or HDMI

## Slide 6: Software Design
Python Module consists of:
  Google Assistant default script from their site
  gcalnotifier.py: it retrieves the calendar entries from Google Calendar every minute and notify the user if there are events that starts in the following 10 minutes

## Slide 7: Software Design
gcalnotfier.py contains the following functions:
  get_credentials(): create the credentials in order to access Google Calendar and Google Assistant using the auto-generated file from Google
  has_reminder(event): returns True if there's a reminder set for the event
  get_next_event(search_limit): get all the events on the calendar from now through 'seach_limit' minutes from now
  main():
    infinite loop to continuously check Google Calendar for future entries and if there are any notify the user how much time is left until the event starts
    It does 3 notifications, one for 10-5 minutes remaining, one for 5-2 minutes remaining and a less than 2 minutes remaining

## Slide 8: Results and further work Current version of the project
Reliable calendar entries polling
Notifications via HDMI sound card
Google Assistant functionalities
Add calendar events using Google Assistant

## Slide 9: Results and further work Extensions and Improvements
AUX or USB sound card notification (no dependency of a monitor)
Custom calendar view using an old monitor (can be mounted on a wall)
Custom notification for every event (using TTS to notify the event title)

## Slide 10: References
https://developers.google.com/calendar/quickstart/python
https://developers.google.com/assistant/sdk/guides/service/python/embed/audio
https://www.draw.io/